PRODUCT:  Manual standard-duty (SD-10/15) clutch roller shade.  Standard size roller shade designed for small to mid-size window openings.

PART 1 GENERAL

  - SECTION INCLUDES

    - Manual roll-up fabric interior window shades including mounting hardware.

  - RELATED SECTIONS

    - Section 06 10 00 - Rough Carpentry.

    - Section 07 90 00 - Joint Protection.

    - Section 09 21 16 - Gypsum Board Shaft Wall Assemblies.

    - Section 09 51 23 - Acoustical Tile Ceilings.

  - REFERENCES

    - NFPA 701-99 - Fire Tests for Flame-Resistant Textiles and Films.

    - GREENGUARD Environmental Institute Children & Schools

    - US Green Building Council.

  - SUBMITTALS

    - Submit under provisions of Section 01 33 26 - Source Quality Control Reporting:

    - Product Data:  Manufacturer's data sheets on each product specified, including:

- Preparation instructions and recommendations.

- Installation and maintenance instructions.

- Styles, material descriptions, dimensions of individual components, profiles, features, finishes and operating instructions.

- Storage and handling requirements and recommendations.

- Mounting details and installation methods, including integration of hardware with building structure.

    - Shop Drawings:  Plans, elevations, sections, product details, installation details, operational clearances, and relationship to adjacent work.

    - Window Treatment Schedule:  For all roller shades.  Use same room designations as indicated on the Drawings, field verified window dimensions, quantities, type of shade, controls, fabric, and color, and include opening sizes and key to typical mounting details.

    - Selection Samples:  For each finish product specified, two complete sets of shade cloth options and finish color samples representing manufacturer's full range of available colors and patterns.

    - Verification Samples:  For each finish product specified, two complete sets of shade components, unassembled, demonstrating compliance with specified requirements.  Shade fabric sample and finish sample as selected, representing actual product, color, and patterns.  Mark face of material to indicate interior faces.

    - Maintenance Data:  Methods for maintaining roller shades, precautions regarding cleaning materials and methods, instructions for operating hardware and controls.

    - Manufacturer's Certificates: Certify products meet or exceed specified requirements.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Obtain roller shades through one source from a single manufacturer with a minimum of twenty years’ experience in manufacturing products comparable to those specified in this section.

    - NFPA Flame-Test: Passes NFPA 701. Materials tested shall be identical to products proposed for use.

    - Mock-Up:  Provide a mock-up of one of each type roller shade assembly specified for evaluation of mounting, appearance and accessories.

- Locate mock-up in window(s) designated by Architect.

- Do not proceed with remaining work until mock-up is accepted by Architect.

  - DELIVERY, STORAGE, AND HANDLING

    - Do not deliver window shades until building is enclosed and construction within spaces where shades will be installed is substantially complete.

    - Deliver products in manufacturer's original, unopened, undamaged containers with labels intact.

    - Label containers and shades according to Window Shade Schedule.

    - Store products in manufacturer's unopened packaging until ready for installation.

  - SEQUENCING

    - Ensure that locating templates and other information required for installation of products of this section are furnished to affected trades in time to prevent interruption of construction progress.

    - Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

  - PROJECT CONDITIONS

    - Install roller shades after finish work and ambient temperature, humidity and ventilation conditions are maintained at levels recommended for project upon completion.

  - WARRANTY

    - Initial warranty:  Provide an initial one-year warranty on all products and services, including installations, to be free from defects. Products or services found to be defective under normal use during this initial warranty period will be repaired or replaced without charge to the customer.  Refer to Blueshade® “Best-in-the-Business” warranty and exclusions.  Warranty period shall begin upon completion of the installation.

    - Extended Warranty: Provide a 25-year limited warranty. Refer to BlueShade® “Best-in-the-Business” warranty and exclusions.

PART 2 PRODUCTS

  - MANUFACTURERS

    - Basis of design: Blueshade by Drapery Industries Inc., Rochester, NY 14610,                       Toll free (844-737-2533), Web: www.blueshade.us.com

Product: Manual standard-duty (SD-10/15) clutch roller shade.

    - Substitutions: Requests for substitutions will be considered in accordance with provisions of Section 01 60 00.

  - MANUAL WINDOW SHADES

    - Manually operated vertical roll-up shade with fabric, clutch, chain, and necessary hardware to complete installation.  BlueShade standard-duty (SD-10/15) series as manufactured by Drapery Industries Inc.

- Operation:  Bead chain and clutch operating mechanism allowing shade to stop when chain is released. Designed never to need adjustment or lubrication. Provide limit stops to prevent shade from being raised or lowered too far.

  - Clutch mechanism: Bi-directional mechanical clutch fabricated from high carbon steel and molded fiberglass reinforced polyester or injected molded nylon, comprised of multi-banded, steel springs; size determined by width, height of shade and weight of fabric selected. Velvetrol internal spring arrangement to provide smooth operation.  White & Black color as selected by Architect.

  - Bead chain loop: Stainless steel bead chain hanging at side of window.

  - Bead Chain Hold Down: Spring-Loaded Tensioner (optional). Color as selected by Architect in Gray, White, Vanilla, Bronze or Black.

  - Idler Assembly: Provide roller idler assembly of molded nylon spring-loaded length idler pin to facilitate easy installation, and removal of shade for service.

- Roller tube: Fabricated from extruded aluminum, steel is not acceptable. Diameter, wall thickness, and material selected by manufacturer to accommodate shade size with minimum deflection.  Fabric Connection to roller tube with LSE (low surface energy) double sided adhesive specifically developed to attach coated textiles to metal.

- Mounting:  mounting brackets fabricated from stamped steel with powder coated finish. Color as selected by Architect in Anodized, White, Vanilla, Bronze or Black.

    - Fabric Length: Provide a minimum of 12" greater than window height.

    - Shade slat: Aluminum slat 1/8” x 1” MF encased in welded heat seamed hem.

    - Orientation: Regular (from back of roller) or reverse roll.

  - FABRIC

    - Color and pattern:  __________, No. _____.

    - Color and pattern: As indicated in Color Schedule on Drawings.

    - Color and pattern: As selected by Architect from manufacturer's full range.

PART 3 EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of another sub-contractor, notify Architect of unsatisfactory preparation before proceeding.

  - PREPARATION

    - Coordinate requirements for blocking and structural supports to ensure adequate means for installation of pocket enclosure brackets, and hardware for installation of manual window shades.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions.

    - Install roller shades level, plumb, square, and true.  Allow proper clearances for window operation hardware.

    - Install after interior construction is essentially complete.

    - Remove and properly dispose of all debris and metal shavings.  Vacuum as necessary.

  - TESTING AND DEMONSTRATION

    - Test window shades to verify that controls, limit stops, interface to other building materials, and other operating components are functional. Correct deficiencies.

    - Demonstrate operation of shades to Owner's designated representatives.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

  - SCHEDULES

    - Refer to Drawings for shade types and locations.

END OF SECTION

# Text boxes

Specifiers: for more information

please contact us at:

www.blueshade.us.com

Toll Free: 844-737-2533